Function	Potential Failure Mode	Effect	Cause	Severity	Occurrence	Detection	RPN	Mitigation
Motor moves pointer to target	Pointer overshoots or undershoots	Missed target, user confusion	Poor PID tuning	7	5	4	140	Tune PID gains, add position feedback
Rail movement	Jamming or stalling	Incomplete motion, system halt	Debris or misalignment	6	4	3	72	Clean rail, align track, add limit switches
Electrical system	Overcurrent or overheating	Damage to motor or driver	Excessive load or poor ventilation	8	3	5	120	Add thermal cutoff, fuse, monitor current
GUI selection	Wrong target selected	Incorrect motion	Software bug or user error	5	3	4	60	Validate input, add confirmation step
Mounting	Pointer detaches during motion	Safety hazard	Weak adhesive or loose fasteners	9	2	6	108	Use mechanical fasteners, test under load

Severity Down/ Occurrence Right	1 - Rare	2 - Unlikely	3 - Possible	4 - Likely	5 - Frequent
9 - Catastrophic		Pointer detachment
8 – Very Serious					Overcurrent/Overheating
7 - Serious					Overshoot/Undershoot
6 - Moderate				Rail jamming
5 - Minor			GUI selection error